## Slide 1
Evaluation of Modern Irrigation Project
1Department of Civil engineering, Zagazig University, Zagazig, Egypt.
Introduction
Drip irrigation​ A type of localized irrigation in which drops of water are delivered at or near the root of plants.
Lateral irrigation system
It is one of the modern irrigation methods . In this type the filed takes the form of a circle. This type of irrigation is used to irrigate filed crops
Water Source in Egypt
Amount of water =Billon m³/ year
Modern irrigation system materia
Pvc pipe Dripper
Valves water hammer
Drip irrigation pivot irrigation
Anshas orchard site study , it is located in Sharkia Governorate, delta Egypt, its geographical coordinates are 30° 30' 10" North, 31° 33' 27" East . with an area 2117 fedden.
Prof. Asst :Ahmed Helmey Prof. Asst : Sayed Mukhtar
Prof. Asst : Ismail Abd-Elaty Prof. Asst : Ismail Fathy
Design criteria
Hazen Williams : V = 0.355C D0.63 (H/L)0.54
continuity equation : Q = A * V , Check velocity =Q/A
Pump capacity HP =ɣ*H*Q /75η , Pw = .746H/ η
the Blaney- Criddle method =192*K*P*(T+17.3)/100 ( m3 /fed / month )
Hargreaves method =180*K*C*d*T ( m3 /fed / month)
Results
pivot irrigation network | Drip irrigation network | 
26.1 m3 /day | 25.89 m3 /day | Water consumption per feddan
5669 m3 /day | 8035 m3 /day | Total water consumption
4,791,568 LE | 13,549,390 LE | Total Cost
Recommendation
A cost study is being done Detailed project cost calculation
2. Software is used to design networks and accurately calculate velocities and pressures
3. In the case of hot areas and times, irrigation should be done at low temperatures or at night
4. Studying the use of different irrigation systems such as sub-surface irrigation
5. Studying the use of different materials for pipes and calculating the difference in losses and costs
6. Calculate the return of each project
Agriculture criteria drip irrigation
Height | Water duty | distance | Crop
3 – 6 m | 50 | 2*4 | Mango
6 – 12 m | 100 | 2*2 | Palm
6 – 12 m | 60 | 1*1 | Casuarina
Conclusion
  A drip and pivot irrigation network has been designed
  Velocities, pressures, disposals, water quantity and losses were calculated for each irrigation network
  The amount of water consumed in the drip and pivot irrigation networks was compared
  Calculation and comparison of drip and pivot irrigation network prices
  Calculate and compare evaporation and transpiration rates
Water supply =79.2
River Nile=55.5
Rain = 1.3
Ground water =8.2
Reuse of sanitary =13.5
Desalination of sea water =.7
Water demand =91
Agriculture = 65
Domestic =11
Evaporation = 10
Industrial =5
Shortage =11.8
Agriculture criteria pivot irrigation
Height | Water duty | Distance | Crop
40-60 cm | 23.4m3/ fed/day | 15 cm | Wheat
120-220 cm | 26.1m3/ fed/day | 30 –40cm | Maize
6-12 m | 100L/day | 2*2 m | Palm
6- 12 m | 60 L/day | 1*1 m | Casuarina
Ahmed Mohamed Atef Ebrahim Mohamed Elsayed
Mohamed Ashraf Abd elslam Abdalrashid Saeed Soliman
Abdelwahab Amged Elsayed Ahmed Ali Bakhtroh